## Slide 1
MILITARY INSTITUTE OF SCIENCE & TECHNOLOGY
DEPARTMENT OF
AERONAUTICAL ENGINEERING

## Slide 2
DESIGN, ANALYSIS AND FABRICATION OF A FULLY ARTICULATED HELICOPTER’s MAIN ROTOR SYSTEM

## Slide 4
SUPERVISED BY:
Gp. Capt. A L Golani, IAF
Professor (Senior Instructor)
Department of Aeronautical Engineering (AE)
Military Institute of Science and Technology (MIST)

## Slide 5: TEAM MEMBER
SAMIN YASER AHMED
ARAFAT AHMED
NAZIB EADIN
SABRINA SAYEDA AMIN
ABU SALEH MD. MUHID
TAIMUM AL-NAFIS
SHAMIM FERDOUS ZADID
201622025
20162239
201622047
201622051
201522043
201522049
201422058

## Slide 6: OBJECTIVES
Design and Fabrication
Change pitch and Angle of Attack (AOA)
Demonstrating basic movements(Collective Pitch & Cyclic Pitch) of the rotor blades
Measuring the lift generated for different RPMs and angle of attacks (AOA)
Force Calculation

## Slide 7
DESIGN, ANALYSIS AND FABRICATION OF A FULLY ARTICULATED HELICOPTER’s MAIN ROTOR SYSTEM

## Slide 8: PROCESSES FOLLOWED
Understanding the basic helicopter mechanism.
Designing it in Solidworks.
Fixing the calculation.
Finalizing the measurement.
Validating it on Ansys.
Fabrication.
Controlling Mechanism.
Painting

## Slide 9: REFERRED BOOKS FOR THEORY
John M. Seddon and Simon Newman “Basic Helicopter Aerodynamics’’
Alfred Gessow and Garry C. Myers “Aerodynamics of the Helicopter”
Johnson, Wayne “Helicopter theory”

## Slide 10: MAIN ROTOR SYSTEM OF HELICOPTER
A helicopter main rotor system is the combination of
Rotor blades
    Generates Lift
Control system
    Collective Pitch Control
    Cyclic Pitch Control
    RPM Of Blades

## Slide 11: BASIC PARTS OF MAIN ROTOR SYSTEM

## Slide 12: Design of Blade
Selected Airfoil: NACA 0012
FEATURES :
Symmetric Airfoil (Ease in Manufacture)
Optimum Thickness
Low pitching moment co-efficient

## Slide 13
Selected Airfoil: NACA 0012
    FEATURES :
    Stall Angle: 15° (approx.)
    Smooth Curve Of CL Vs Alpha
Cl
Alpha

## Slide 14: Calculation

## Slide 17
Power = 244.17 W
Power in HP = 0.3
Used Motor RPM =800
Power = 0.4 HP

## Slide 18: MAIN ROTOR CONTROLS
Cyclic blade control:
used to change a helicopter's roll and pitch
By tilting swashplate AOA can be varied
Negative AOA at the advancing blades & positive AOA at the retreating blades
Collective blade control:
To control the collective pitch of the main rotor blades
By lifting swashplate without tilting it
All blades need to have same AOA

## Slide 19: FULLY ARTICULATED JOINTS
FLAPPING:
Flapping is the vertical movement of a blade up or down to increase or decrease lift in order to compensate for dissymmetry of lift.
FEATHERING:
Feathering changes blade angle (pitch) and influences the blade's angle of attack.
A blade feathers along its longitudinal axis, and a bearing is usually used to support this.
LEAD LAG:
Leading and lagging is the horizontal movement of the rotor blades forwards and backwards along a vertical hinge.
It reduces the stress on the rotor system due to blade flapping

## Slide 20: CAD DESIGN
Swash Plates:
Fig: 3D view of Upper and Lower Swash Plate.
Fig: Swash Plate Assembly.

## Slide 21: CAD DESIGN
Final Base Assembly:
Fig: 3D view of Base Assembly.

## Slide 22: CAD DESIGN
Articulated Joints Assembly:
Fig: Articulated Joints.

## Slide 23: CAD DESIGN
Conventional Articulated Joints Assembly:
Fig: Articulated Joints.

## Slide 24: CAD DESIGN
Hub:
Fig: 3D view of Hub

## Slide 25: CAD DESIGN
Articular Joint:
Blade:
Fig: 3D View of Articular Joint.
Fig: 3D View of Blade.

## Slide 26: CAD DESIGN
Linkage-Rod Assembly:
Fig: 3D view of Linkage-Rod Assembly.

## Slide 27: CAD DESIGN
Final Assembly of the System:
Fig: 3D view of Final Assembly of the system.

## Slide 28: FABRICATION OF ROTOR MECHANISM
  Selection Process:
FIGURE OF MERIT

## Slide 29
Manufacturing of Parts:
  Upper swash plate:
    Material Used: Mild Steel
    Manufacturing Technique: Turning, Facing, Sanding.
    Machine Used: Lathe Machine.
    Dimension: 124.69 mm outer diameter and 88 mm inner diameter and with a height of 15 mm.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Upper Swash Plate.

## Slide 30
Manufacturing of Parts:
  Lower swash plate:
    Material Used: Mild Steel
    Manufacturing Technique: Turning, Facing, Sanding.
    Machine Used: Lathe Machine.
    Dimension: 150 mm outer diameter and 78 mm inner diameter and with a height of 15mm.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Lower Swash Plate.

## Slide 31
Manufacturing of Parts:
  Mast:
    Material Used: Mild Steel
    Manufacturing Technique: Cutting.
    Machine Used: Cutting Machine.
    Dimension: Hollow shaft with diameter of 18 mm and length 330 mm.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Mast.

## Slide 32
Manufacturing of Parts:
  Motor Base:
    Material Used: Mild Steel
    Manufacturing Technique: Welding. Cutting.
    Machine Used: Arc Welding Machine. Cutting machine.
    Dimension: 250 mm of Length, 180 mm of Width and Thickness 3 mm.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Motor Base.

## Slide 33
Manufacturing of Parts:
  Connecting Rod:
    Material Used: Mild Steel
    Manufacturing Technique: Cutting.
    Machine Used: Cutting machine.
    Dimension: 180 mm of Length and diameter of 10 mm.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Connecting Rod.

## Slide 34
Manufacturing of Parts:
  Articular Joint:
    Material Used: Mild Steel
    Manufacturing Technique: Cutting, Drilling and CAD/CAM interface.
    Machine Used: Cutting machine, Drilling Machine and CNC machine.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Articular Joint.

## Slide 35
Manufacturing of Parts:
  Base:
    Material Used: Mild Steel
    Manufacturing Technique: Cutting, Fitting, Riveting and Welding.
    Machine Used: Cutting machine, Arc Welding.
    Dimension: 600 mm of Length, Width of 300 mm and thickness of 3 mm.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Base.

## Slide 36
Manufacturing of Parts:
  Rotor Blade:
    Material Used: Mild Steel, Wood.
    Manufacturing Technique: Cutting, Welding and Drilling.
    Machine Used: Cutting machine, Arc Welding and Drilling Machine.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Rotor Blade.

## Slide 37
Manufacturing of Parts:
  Rotor Hub:
    Material Used: Mild Steel
    Manufacturing Technique: CAD/CAM interfacing, Drilling.
    Machine Used: CNC Machine and Drilling Machine.
    Dimension: 70 mm of diameter , 3 pair of 35 mm tooth Length and 17 mm of height.
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Rotor Hub.

## Slide 38: FABRICATION OF ROTOR MECHANISM
Manufacturing Process:

## Slide 39
Final Assembly:
FABRICATION OF ROTOR MECHANISM
Fig: Fabrication Process of Rotor Hub.

## Slide 40
Guidelines: CFD validation dictates process how model went from a CAD-model to a discretized volume mesh generated in Ansys. The results are gathered from the simulations and indicate significant results from the CAD design, meshing and simulations.
CFD VALIDATION
CAD Modeling:
Domain in PBC Method
Domain in Cylindrical Method.

## Slide 41
Meshing:
CFD VALIDATION
Cross-Section of Domain in PBC Method.
Cross-Section of Blade.

## Slide 42
Flight Simulations in Hovering Mode:
CFD VALIDATION
Velocity Vector on Blade at 5 deg Pitch and 50 RPM

## Slide 43
Flight Simulations in Hovering Mode:
CFD VALIDATION
Velocity Streamline in Domain at 5 deg Pitch and 50 RPM

## Slide 44
Limitations:
  Limited Time
  Shortage of Raw Materials
  Unavailability of High-Tech Machinery
  Limited Funding
CONCLUDING REMARKS
Recommendations:
  Use of Composite materials
  Use of Balsa wood in manufacturing wing
  Use of better equipment
  Designing of tail rotor system to develop complete
  helicopter

## Slide 45
Demonstration of Our Capstone Project